EE445L – Lab 9: Temperature Data Acquisition System
Michael Park and Jack Zhao
04/18/16

1.0 OBJECTIVE
The objective of this lab is to design, build and test a digital thermometer that can measure the range of 10 to 40 ˚C using an ADC converter on the TM4C123. Educationally, we are learning how to create a temperature acquisition circuit using a Whitestone Bridge circuit, instrumentation amplifier, and a butterworth low-pass filter as well as how to choose a sampling frequency (Nyquist Theorem, Valvano Postulate) and a cutoff frequency for the filter.

2.0 HARDWARE DESIGN
Figure 1: Circuit diagram of the thermistor interface

3.0 SOFTWARE DESIGN
1) Calibration data (procedure 5 and the calib.h file)

2) Low level ADC interface (ADC.c and ADC.h files)

3) Main program used to measure temperature

4.0 MEASUREMENT DATA
1) Sketch three waveforms (procedure 1)

2) Static circuit performance (procedure 2)

3) Dynamic circuit performance (procedure 3)

4) Accuracy (procedure 6)

5) Reproducibility (procedure 7)

5.0 ANALYSIS AND DISCUSSION
1) What is the Nyquist theorem and how does it apply to this lab?
Nyquist theorem states that the sampling frequency should be at least twice the frequency of the signal to be sampled. In this lab, the frequency component of the measured signal was between 0 – 10 Hz. Therefore the sampling frequency of our system had to be at least 20 Hz.

2) Explain the difference between resolution and accuracy?
Resolution is the smallest change in the input parameter that can be reliably detected by the measurement. Accuracy ((Actual – Ideal) / Ideal) is a measure of how close our instrument measures the desired parameter referred to the NIST.

3) Derive an equation to relate reproducibility and precision of the thermometer.
Reproducibility is a parameter that specifies whether the instrument has equal outputs give identical inputs over some period of time. This parameter can be expressed as the full range of output results given a fixed input. Thus, the precision of the thermometer can be expressed as the following equation.
Precision = full range of output results at fixed input / resolution of the thermometer.

4) What is the purpose of the LPF?
The purpose of the LPF is to remove high frequency noise to improve signal to noise ratio. In this lab, our frequency of interest was 0 – 10Hz (low frequency). Thus using a butterworth LPF(Anti-ailiasing filter) restricted the bandwith of the signal, and as a result, increased the signal to noise ratio (SNR).

5) If the R versus T curve of the thermistor is so nonlinear, why does the voltage versus temperature curve look so linear?
The R versus T curve of the thermistor is nonlinear becuase the transducer(thermistor) is nonlinear. However, the bridge circuit used for the thermistor is also nonlinear as shown by the equation (2.5*Rt)/(R1+Rt). Therefore, because both the transducer and the circuit are nonlinear, the final outcome (voltage vs temperature curve) becomes much closer to being linear.

6) There are four methods (a,b,c,d) listed in the 4) Software Conversion section of methods and constraints. For one of the methods you did not implement, give reasons why your method is better, and give reasons why this alternative method would have been better.
We used a small table lookup (≈50 entries) with linear interpolation in between instead of a large table lookup (one entry for each ADC value). Small table lookup takes up less memory space than the large table lookup. On the other hand, large table lookup is more accurate because it does not use linear interpolation.